Concurrent and Distributed Devices (CDD101)
Dr. Joseph Kehoe

---
Performance Theory
- Latency
  - Total time it takes to compute a single result
  - Measured in units of time
- Throughput
  - The rate at which a series of results can be computed
  - Measured in units of work per unit time
- Power Consumption
  - The amount of power required to performa computation
  - Measured in Work per power unit

---
Speedup
- Compares latency in solving an indentical problem on one hardware unit versus P hardware units
  - Sp=T1/Tp
- Absolute Speedup
  - Sequential Algorithm Time used for T1
- Relative Speedup
  - Parallel algorithm used for T1

---
Efficiency
- Speedup divided by number of workers
  - Sp/P
  - T1/P*Tp
- Ideal efficiency is 1
  - 100% efficiency

---
Superlinear Speedup
- Parallel Algorithm makes better use of cache
- Parallel Algorithm is better
- Parallel Algorithm with multiple threads uses cache better than single parallel algorithm execution

---
Amdahl’s Law
- Work is of two types
  - Serial Work
    - Cannot be parallelised
  - Parallel Work
    - Can be done in parallel
- T1=Workserial + Workparallel
- Tp>=Workserial+Workparallel/P

---
Amdahl’s Law
- If f is the fraction of the total work that is serial then (1-f) is the fraction that is parallel
  - Wserial=fT1
  - Wparallel=(1-f)T1
- Sp<= 1/ [f+(1-f)/p]
- As P -> infinity
  - Seedupinf<= 1/f

---
Gustafson-Barsis’ Law
- Amdahl’s Law viewed program size as fixed and the processor count as variable
  - But program size can increase as processor count increases
- Sometimes the serial part remains constant as the program size increases
  - Thus allowing for greater speedup

---
Work-Span Model
- Tasks form an acyclic graph
  - Ignores communication and memory access costs
  - Assmes task scheduling is greedy
- T1: time required for serial version of algorithm to run
  - Known as Work
- Tinf: time required for algorithm to run on ideal computer with infinite processors
  - Known as Span

---
Work-Span Model
- Span is equivalent to the length of the critical path
  - Aka depth, step complexity
- Superlinear speedup is impossible in the Work-Span Model
  - Sp=T1/Tp
  - T1/Tp<=T1/(T1/P) = P
  - Therefore Sp<=P

---
Work-Span Model
- Adding new processors never slows down an algorithm
  - Assuming greedy scheduling
  - Sp=T1/Tp <=T1/Tinf
- Brent’s Lemma
  - Tp <= (T1-Tinf)/P + Tinf if Tinf << T1
- When working on parallelism focus on the span
- Increase work only if it decreases the span